## Slide 1: High Performance I/O with NUMA Systems in Linux
Lance Shelton
Notes: ----- Meeting Notes (5/10/13 16:04) -----
Additional info is provided in this section for some slides.

## Slide 2: How prevalent is NUMA?
All major vendors
  HP, Dell, IBM, Cisco, SuperMicro, Hitachi, etc.
As small as 1U
2, 4, and 8 socket systems
2 to 10 cores per socket
Number of cores doubles with HyperThreading
8 x 10 x 2 = 160 CPU cores
NUMA is mainstream.
FUSION-IO
FUIO
N-IO

## Slide 3: Why use large NUMA servers?
NUMA is key to the current evolution of performance
  Storage rates are drastically increasing
  Processor speeds are stagnant
  Multi-core cannot scale infinitely without NUMA
NUMA meets the needs of the application
  No partitioning is required
  Faster than clustering multiple servers
  Works well in combination with scale out
FUSION-IO
FUIO
N-IO

## Slide 4: Nodes, Sockets, Cores, Threads
FUSION-IO
FUIO
N-IO
Memory
Socket
NUMA Node
Cores
Threads
+
=

## Slide 5: Non-Uniform I/O Access
FUSION-IO
FUIO
N-IO
I/O = PCIe
Internal flash
Host bus adapter
to storage network
Notes: ----- Meeting Notes (5/10/13 16:05) -----
In addition to memory access, I/O access is also non-uniform.

## Slide 6: 2, 4, and 8 Socket Servers
# numactl --hardware
node 0 1 2 3 4 5 6 7
0: 10 12 17 17 19 19 19 19
1: 12 10 17 17 19 19 19 19
2: 17 17 10 12 19 19 19 19
3: 17 17 12 10 19 19 19 19
4: 19 19 19 19 10 12 17 17
5: 19 19 19 19 12 10 17 17
6: 19 19 19 19 17 17 10 12
7: 19 19 19 19 17 17 12 10
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:05) -----
pictured: HP DL380p, DL580, DL980 (up to 160 CPU threads); numactl displays the distance between NUMA nodes

## Slide 7: Enterprise Storage
Clients
Storage
Database Servers
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:05) -----
Storage is connected to the database servers via FibreChannel, Infiniband, or iSCSI. Database servers are connected to clients via Ethernet. Without optimizing database servers, backend storage performance is not fully realized.

## Slide 8: PCIe Local Nodes
I/O Hub
Intel Sandy Bridge
Intel Nehalem
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:06) -----
I/O Hubs and sockets are connected via QPI. Westmere arch is the same as Nehalem. Ivy Bridge is the same as Sandy Bridge.

## Slide 9: PCIe Local Nodes
# cat /sys/devices/pci0000:50/0000:50:09.0/numa_node
0
Only one local node is presented to the OS
I/O Hub
Intel Sandy Bridge
Intel Nehalem
X
FUSION-IO
FUIO
N-IO
X
Notes: ----- Meeting Notes (5/10/13 16:06) -----
Note that the second QPI link from the I/O Hub will still be used, it is just not recognized as a local connection.

## Slide 10: PCIe Local Node?
# cat /sys/devices/pci0000:50/0000:50:09.0/numa_node
-1
Not detected? Update the BIOS.
I/O Hub
Intel Sandy Bridge
Intel Nehalem
FUSION-IO
FUIO
N-IO
?
?
?
?
Notes: ----- Meeting Notes (5/10/13 16:06) -----
NUMA info is provided by the System Locality Information Table (SLIT) in ACPI.

## Slide 11: Localizing I/O from Storage
50-100% performance improvement vs. non-NUMA aware volume placement
FUSION-IO
FUIO
N-IO

## Slide 12: Localizing I/O – High Availability
Node locality of volumes must still be maintained
FUSION-IO
FUIO
N-IO

## Slide 13: Localizing I/O – HA Failover
Node locality maintained
All available ports are still used
FUSION-IO
FUIO
N-IO

## Slide 14: Localizing I/O – Components
HBA placement
Interrupt affinity
Kernel thread affinity
Application affinity
Analyze everything in the data path.
Localize all components to the HBA local nodes.
Reduces latency and improves caching
FUSION-IO
FUIO
N-IO

## Slide 15: Discovering Device Locality
Devices associated with each volume
  multipath –ll
  ls -d /sys/bus/pci/devices/*/host*
Device location
  dmidecode -t slot
  lspci -tv
NUMA node of devices
  /sys/devices/pci*/*/numa_node
FUIO
N-IO
FUSION-IO
?
?

## Slide 16: Pinning Interrupts
Pin IRQs to the local node
Distribute IRQs between cores in the local node
# grep [driver] /proc/interrupts
[num]: ...
# cat /proc/irq/[num]/node
[node]
# echo [CPU mask] > /proc/irq/[num]/smp_affinity
~100% improvement
Reduces latency & CPU contention, improves caching
FUSION-IO
FUIO
N-IO
120
122
121
123
…
Notes: ----- Meeting Notes (5/10/13 16:07) -----
These settings are not persistent

## Slide 17: Persistently Pinning Interrupts
irqbalance: run-time load balancing
  Mixed results
  Better with RHEL 6.4 + kernel update + Sandy Bridge
Customized init service to set affinity on boot
  Best results for a known application
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:07) -----
Some IRQs perform better when grouped, while extremely high-usage IRQs perform best on separate cores. In some cases, tuning for bandwidth requires a different grouping than tuning for IOPS.

## Slide 18: Driver Kernel Thread Affinity
Sometimes handled by Linux drivers
Verify and adjust
# taskset -p -c [cpumask] [pid]
pid [pid]'s current affinity list: 0-159
pid [pid]'s new affinity list: 20-29
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:07) -----
Sometimes kernel threads cannot be pinned from userspace.

## Slide 19: Block Device Tuning
# echo noop > /sys/block/[device]/queue/scheduler
  10% improvement
# echo 0 > /sys/block/[device]/queue/add_random
  10% improvement
# echo 2 > /sys/block/[device]/queue/rq_affinity
  5% improvement
# echo [0 or 1] > /sys/block/[device]/queue/rotational
  Mixed results
  Reduces latency and CPU utilization
FUIO
N-IO
FUSION-IO
Notes: ----- Meeting Notes (5/10/13 16:08) -----
Flash storage latency is fairly consistent and thus does not provide a useful contribution to the entropy pool (add_random). Rotational seems to impact how adjacent small I/Os are combined, in a way that is in some cases beneficial to non-rotational devices.

## Slide 20: Persistent Block Device Tuning
udev rules (/etc/udev/rules.d/)
  I/O devices
  ACTION=="add|change", SUBSYSTEM=="block", ATTR{device/vendor}=="FUSIONIO", ATTR{queue/scheduler}="noop", ATTR{queue/rq_affinity}="2", ATTR{queue/add_random}="0”
  devices with I/O slave devices (DM multipath)
  ACTION=="add|change", KERNEL=="dm-*", PROGRAM="/bin/bash -c 'cat /sys/block/$name/slaves/*/device/vendor | grep FUSIONIO'", ATTR{queue/scheduler}="noop", ATTR{queue/rq_affinity}="2", ATTR{queue/add_random}="0"
Note: udev rules may only rely on sysfs parameters that are available at the time the device is created.
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:08) -----
The udev daemon runs when the KOBJ_ADD uevent fires, which is triggered by device_register(). Use of any sysfs files created after device_register() may introduce race conditions in udev rules.

## Slide 21: Power/Performance Tuning
Disable c-states in the BIOS
Disable c-states in the boot loader (grub)
  intel_idle.max_cstate=0
  processor.max_cstate=0
10% improvement
Keeping processors in active states reduces latency
FUSION-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:08) -----
Only one of these methods is necessary, but it varies from platform to platform. Verify that /sys/devices/system/cpu/cpu0/cpuidle does not exist to be sure.

## Slide 22: Application Tuning
OS-provided tools
  taskset
  cgroups
  numad
Application-specific settings
  Oracle
    _enable_NUMA_support
FUIO
N-IO
FUSION-IO

## Slide 23: Benchmarking Performance
Test thread affinity
  FIO
    cpus_allowed
    numa_cpu_nodes
    numa_mem_policy
  Oracle Orion and others
    taskset -c [cpulist] [test command]
Measuring performance
  iostat
  Application-specific
FUSION-IO
FUIO
N-IO

## Slide 24: 8 Socket Total Performance Gains
4k block size iops
Chart: 
| Reads | Writes
Untuned | 200000 | 180000
Tuned | 704000 | 633000
READS WRITES
FUSION-IO
N-IO
FUIO
N-IO
Notes: ----- Meeting Notes (5/10/13 16:09) -----
Even greater gains in performance are possible - this configuration was tuned up to the limitations of the hardware. Further gains are in development.

## Slide 25: Tools for NUMA Tuning
  numactl cgroups
  taskset lstopo
  dmidecode sysfs
  irqbalance numad
  top numatop
  htop tuna
  irqstat tuned-adm
FUSION-IO
FUIO
N-IO

## Slide 26: top: terminal is not big enough
(top in RHEL 6.4)
FUSION-IO
FUIO
N-IO

## Slide 27: mpstat with 160 cores
FUSION-IO
FUIO
N-IO

## Slide 28: /proc/interrupts with 160 cores
FUSION-IO
FUIO
N-IO

## Slide 29: top: added NUMA support
https://gitorious.org/procps/procps
FUSION-IO
FUIO
N-IO

## Slide 30: irqstat: IRQ viewer for NUMA
https://github.com/lanceshelton/irqstat
FUSION-IO
FUIO
N-IO

## Slide 31: Must end users be NUMA-aware?
Unfortunately, yes.
  Users must be aware of PCIe device slot placement
  Optimal NUMA tuning is not yet performed by the OS
  Persistent tuning is a non-trivial task
  Performance challenges are changing faster than tools
FUSION-IO
FUIO
N-IO

## Slide 32: How can this be improved?
  NUMA architectures must be detected properly and tuned by default
    Phase out Nehalem or add SLIT support for multiple local nodes
  Linux distributions need to provide optimal tuning across applications and devices at the OS level
  Improve existing tools
FUSION-IO
FUIO
N-IO

## Slide 33: What’s next?
More cores per socket
  15 core CPUs by the end of next year?
Removal of existing bottlenecks
  Multi-queue block layer: http://kernel.dk/blk-mq.pdf
Improved tools
  numatop: https://01.org/numatop
  top: https://gitorious.org/procps/procps
  irqstat: https://github.com/lanceshelton/irqstat
FUSION-IO
FUIO
N-IO

## Slide 34: References
HP DL980 Architecture
    http://h20195.www2.hp.com/V2/GetPDF.aspx/4AA3-0643ENW.pdf
HP NUMA Support
    http://bizsupport1.austin.hp.com/bc/docs/support/SupportManual/c03261871/c03261871.pdf
Performance profiling methods
    http://dtrace.org/blogs/brendan/2012/03/07/the-use-method-linux-performance-checklist/
FUSION-IO
FUIO
N-IO

## Slide 35
LShelton@fusionio.com